# How To Take a Compass Bearing

Taking a direction bearing from an ‘O’ map - 3 simple steps.

# Text boxes

- Place the compass on the map so that the long edge of the baseplate joins together your present position with your destination. Check that the direction-of-travel arrow is pointing towards your destination.

2. Keep the baseplate firm on the map and turn the compass housing until the orienting lines are parallel to the north-south lines on the map.  Then check that the orienting arrow is pointing to north on the map.

- Lift the compass off the map. Hold it horizontal by the short end so that it sticks out in front of your waist. Turn yourself and the compass until the red end of the needle points to the north mark on the housing dial. Look up over the compass and you will be facing the feature you wanted to locate.

Note that in steps 1 and 2 the compass needle can be totally ignored.